## Slide 1: About OF-PI Forwarding Abstract Model & IR Support
Haoyu Song

## Slide 2: Overall Forwarding Abstract Model
MAT Model is a good abstract model
  Easy for hardware-based platform mapping
    Pipeline, distributed memory
    Process engine + search engine
  Easy for software-based implementation
A standalone parser module should not stand outside of the MAT model
  A parser is really just a physical implementation
    There could be not a front parser at all if parsing & processing are mixed together
  Suggest to remove it from the abstract model

## Slide 3: One Way to Support a Front Parser
Parsing is packet processing! Why pick it out?
  POF-FIS is sufficient to describe a parser
    “if/else” instructions or even lookup tables can be used
    Parsed header can be explicitly written into metadata
  If a physical front parser is needed, it can be modeled as the action function of the Table 0 (i.e. the interface table)
    Interface table contains info for all physical port and logical ports
      Easy to handle reparsing with context
Disadvantage of this approach
  High level programming in this style may lead to inefficient implementation on software-based platforms
    Strong implication on the actual implementation architecture

## Slide 4: Second Way to Support a Front Parser
Write a normal MAT pipeline with the necessary parsing embedded in main control program
  If a physical front parser is needed, the compiler can extract it from the main control program
    May need more specific instruction such as “extract”
  If incremental parsing is preferred, the compiler can merge it into table actions
Advantage of this approach
  Portable high level program for all target platforms
note: read/write metadata should be abstracted using just names but not {offset, length}. The actual metadata management is the work of the target-specific compiler

## Slide 5: Components in IR
(Required) Tables
  (required) table type
  (required) key type and key fields (logical tables & physical table mapping)
  (optional) table size
  (optional) parameters used by actions
  (optional) list of supported actions
(Required) Actions
  Programmed in POF-FIS
(Optional) Parsing graph
  Only if a front parser is desired
(Optional) Table dependency graph
  Only if hardware pipeline mapping is needed

## Slide 6: Objects in Abstract Model & IR
Operable objects (writable)
  Table & Table entry
  Packet data (no need to distinguish header and payload in OF-PI)
  Packet Metadata
    Per packet registers
  Flow Metadata (counter, meter, and other global resources)
    Per flow registers
  Timers
Non-operable objects (read only)
  Port
  Queue/buffer (can this be abstracted as virtual port?)
  Event
  Autonomous function (can this be abstracted as virtual port?)

## Slide 7: A Really Simple Abstract Forwarding Model
Ports can be physical or virtual ports
  Including queue/buffer, switch fabric, controller, clone re-entry, recirculation, autonomous function
Action block is the major programming point
  Can derive parser using one of the two approaches
  Can infer table dependency
This model is always for just a single packet
  Cloned packets need to be submitted to some “port”
In
Ports
Tables
Actions
Out Ports