## Slide 1: Some IR Questions
Ben Mack-Crane
Huawei

## Slide 2: What is required in an IR?
Match Action Table definitions
Data definitions
  Packet data (Header)
  Packet metadata
  Global and/or flow table metadata
Action definitions
  Invokable procedures that operate on packets and metadata
Event definitions?
  Are these variable or can we define a fixed set of event types?
    Packet received
    Timer expired
    Condition met (e.g., threshold crossing)

## Slide 3: What are we experimenting with?
Parser
Control Flow
Hardware Abstraction
How is this done with OpenFlow datapath models today? What can we add in the IR and what are the tradeoffs?

## Slide 4: Parse Graph
OpenFlow TTP
Parse graph implicit in OpenFlow
  Or at least unspecified…
Packet formats constrained by table pattern
  Explicit match on protocol ID with fixed value
  OpenFlow match field prerequisites
  Can be further constrained by flow_paths

## Slide 5: Parse Graph
AIR meta.yaml
parser provides a parse graph and protocol ID bindings
  Parse graph is a directed graph connecting parse_state values
  Binds protocol ID field values (select_value)
    Also value_set can be referenced in parser
  Enter parser and reach some parse state
    Accepting and exception states (no exception feature yet)
  Constrains packet structure
    Prevents run-time binding of protocol ID values
      E.g. Controller-defined Ethernet TPID
Can the same information be derived from table definitions?
Can the same constraints be provided in table definitions?
  Depends on run-time flexibility in goto_table?
  Use built-in table entries? Read-only tables?

## Slide 6: Parse Graph
From discussion on 6 Feb 15 call:
Also may need to indicate nesting level of a header
  Each instance is explicitly defined by a separate header definition
  May need more flexible scheme that allows reuse by not requiring a distinct header name per “level”
  Three orthogonal concepts: field name, protocol ID value, location in packet
  How is complexity of required parsing indicated in the IR?
  How would MPLS entropy label be represented (two RFCs for this)?
Tradeoff between
  Requiring a distinct name for each field location in (any) packet
  Allowing a field name to be (re)used in different contexts

## Slide 7: Parse Graph
OF-PI
OF-PI also allows run-time binding
  E.g., as supported by POF and some hardware platforms
How can the IR support both
config-time binding and run-time binding?