## Slide 1
POF Southbound Interface PIF Working Group
Haoyu Song / Huawei August 11, 2015

## Slide 2: POF Ecosystem
POF covers an entire ecosystem,
  programming language (e.g., P4) is a component in this ecosystem
POF ecosystem centered on an open SBI
  Current protocol is based on an extension of OF1.x
  No explicit separation of configuration time and run time
  Forwarding abstraction delivered through a set of primitive instructions
Application
Library
GUI/CLI
High level language/ Compiler
Open Southbound Interface
(OF2.0?)
Device / Driver
Programmable Chip

## Slide 3: Key Objects at POF SBI
Name | Description
Protocol | Define the protocol header fields
Metadata | Define the metadata layout
Table | Define table name, table type, table size, search key, and if the table is a shared table
Table Parameter | Define parameter for each table that can be accessed by table instruction block (aka action)
Instruction Block | Define the actions that will be executed after table matching. Each table entry will point to an instruction block.
Service | Define the table pipeline (similar to control flow)

## Slide 4: POF SBI Objects
Service (Table + Instruction Block) forms the main MAT pipeline
  Instruction block is a piece of code written in primitive instructions
  Equivalent to table action in P4, but more flexible
    No instruction count limits; has conditional branching capability
These lower level objects can be compiled from a high level language such as P4
  Can be considered as a kind of IR
  Don’t care physical implementation, but care physical resource sharing
SBI uses OF messages to download these objects to data plane device
A demo example: ipv4.pofs
  A script can be directly used by controller to drive the interface
  P4 program can be compiled to something similar to this file

## Slide 5: POF SBI Protocol - Message
OFPT_XXX
Support all existing OF1.4 messages
Add new POF-specific messages starting from ID# 101
  Counter messages
  Instruction block message
  POF enable/disable messages
  Service messages
  A few other extensions.
All messages carries the same OpenFlow message header format, some message bodies are modified to fit for POF’s requirement
  E.g., table_mod, flow_mod, etc.

## Slide 6: POF SBI Protocol - Instructions
Editing:
OFPIT_POF_SET_FIELD = 0X8001,
OFPIT_POF_ADD_FIELD,
OFPIT_POF_DEL_FIELD,
OFPIT_POF_CALCULATE_FIELD,
OFPIT_POF_COMPARE,
OFPIT_POF_ALG,
Table & Parsing:
OFPIT_POF_GOTO_TABLE,
OFPIT_POF_GET_TABLE_ENTRY
OFPIT_POF_SET_TABLE_ENTRY,
OFPIT_POF_SET_PACKET_OFFSET,
OFPIT_POF_MOVE_PACKET_OFFSET,
Forwarding:
OFPIT_POF_OUTPUT,
OFPIT_POF_DROP,
OFPIT_POF_TOCP,
OFPIT_POF_COUNTER,
OFPIT_POF_METER,
Control Flow:
OFPIT_POF_ABSOLUTE_JMP,
OFPIT_POF_RELATIVE_JMP,
OFPIT_POF_ CONDITIONAL_RELATIVE_JMP,
OFPIT_POF_BRANCH,

## Slide 7: Summary
POF ecosystem advocates open interface for both data-plane programming (configuration) and operation (runtime)
  Configuration and runtime can be unified to maximize the flexibility
POF SBI is based on OpenFlow 1.4 and adds minimum extensions
  Objects at SBI is a form of IR
P4 can be used as a high level language in POF ecosystem
  P4 program can be compile to POF IR and use POF SBI to program devices