## Slide 1: PIFL: Protocol Independent Forwarding Language
Ajeer Pudiyapura
Kishore Atreya
Ravindran Suresh

## Slide 2: Goals for this slide deck
Introduce the PIFL Language.
The compiler architecture for PIFL.
The generic switch forwarding model.
Provide illustrative examples of PIFL language constructs.
Give examples of language constructs used to define switch primitives.
Present a schema based Intermediate Representation scheme - PIFL IR.
Explore how PIFL IR virtualizes a switch and provides a target for high level languages to write code for.
Examples of how switch primitives are represented in PIFL IR.

## Slide 3: PIFL Architecture
High Level Language
Front End Compiler
Hardware data
PIFL IR
Back End Compiler

## Slide 4: Generic Switch Forwarding Model
Parser
Format Key
Format Key
Format Key
.
.
Lookup Table
Lookup Table
Lookup Table
.
.
Process Result
Process Result
Process Result
.
.
Update/Queue Packet
Format Key
Format Key
Format Key
.
.
Lookup Table
Lookup Table
Lookup Table
.
.
Process Result
Process Result
Process Result
.
.
…
…
…
Incoming packet gets parsed and classified.
Keys into tables are formed depending on packet meta data, possibly in parallel.
Tables are looked up, possibly in parallel.
The results are processed, possibly merging results from different lookups.
During this stage:
  States and Table entries can get updated.
  Packet can be acted upon. (Dropped, Forwarded etc).
  Packets can get replicated.
Multiple stages of lookups/processing can be defined.
Packets can be modified/appended/truncated.
Packets can be queued to go out based on available data.

## Slide 5: PIFL Highlights
High Level Language.
Human writable/readable.
Familiar, C like interface.
Provides ‘natural’ programming constructs:
  Structures and Variables – Defines Packet Headers and Metadata.
  Statements – Allows copy of fields.
  ALU operations – Performs operations like TTL decrement.
  Conditional execution – Matches on field values.
  Directives for sequential and parallel control flow.
Provides constructs to define switch primitives exposed by the PIFL IR.
  PARSER, TABLE, KEY_FORMATTER, LOOKUP, POST_LOOKUP, PACKET_HEADER, LAYER_DATA, PACKET_UPDATE, ENQUEUE
Independent of hardware.
Independent of networking protocols.

## Slide 6: Header Definition Example: Ethernet Header
PACKET_HEADER ethHeader
{
FIELD dMac:48; // Destination MAC Address, 48 bits
FIELD sMac:48; // Source MAC Address, 48 bits
FIELD eType:16; // Ether Type, 16 bits
}
Used to express the format of the various protocol headers.
User can define his own protocol headers.
No assumptions about their functionality in the language.

## Slide 7: Header Definition Example: 802.1q Header
STRUCT dot1qTag
{
FIELD tpid:16;
FIELD priority:3;
FIELD cfi:1;
FIELD vlanId:12;
}
PACKET_HEADER dot1qHeader
{
FIELD dMac:48; // Destitnation MAC Address, 48 bits
FIELD sMac:48; // Source MAC Address, 48 bits
STRUCT dot1qTag; // The 802.1q Tag
FIELD eType:16; // Ether Type, 16 bits
}
Provides structure definitions to group fields together so you can operate on them collectively.

## Slide 8: Header Definition Example: IPv4 Header
PACKET_HEADER ipv4OverDot1qHeader
{
PACKET_HEADER dot1qHeader; // The previous header
FIELD ver:4; // IP Version, 4 bits
FIELD hdrLen:4; // Header Length, 4 bits
FIELD tos:8; // Type of Service
FIELD totLen:16; // Total Length, 16 bits
FIELD id:16; // Fragment Id, 16 bits
FIELD flags:4; // Flags, 4 bits
FIELD fragOffset:12; // Fragment Offset, 12 bits
FIELD ttl:8; // Time to Live, 8 bits
FIELD protocol:8; // Protocol
FIELD hdrCksum:16; // Header checksum, 16 bits
FIELD sourceIp:32; // Source IP Address, 32 bits
FIELD destIp:32; // Destination IP Address, 32 bits
}
Allows nesting of definitions.

## Slide 9: Metadata Definition Example: Static Context
STATIC_CTX
{
inputPort; // input port of the packet.
...
...
}
Used to represent preliminary information about the packet
Populated by the hardware when a packet arrives
Hardware compilers need to recognize and implement these
Since this is definition cannot be instantiated, the elements have global scope

## Slide 10: Metadata Definition Example: Dynamic Context
DYNAMIC_CTX
{
FIELD pktCmd:4; // The command that should be applied to this packet
FIELD packetTemplate:8; // classification of the packet, 8 bits
FIELD egressInterface:16; // outgoing interface for the packet
FIELD egressQueueId:8;// queue id for egress
...
...
}
Used to represent additional information about the packet, derived during processing.
Completely user defined.
Populated, used and possibly updated during pipeline stages.
Since this is definition cannot be instantiated, the elements have global scope.

## Slide 11: Metadata Definition Examples: Layer Data
LAYER_DATA ethLayer
{
FIELD dMac:48; // Destination MAC Address, 48 bits
FIELD sMac:48; // Source MAC Address, 48 bits
...
...
}
LAYER_DATA dot1qEthLayer
{
FIELD dMac:48; // Destination MAC Address, 48 bits
FIELD sMac:48; // Source MAC Address, 48 bits
STRUCT dot1qTag; // The 802.1q Tag
...
...
}
Used to define meta data related to packet headers.
Completely user defined.
May contain data extracted from packet header.

## Slide 12: Metadata Definition Examples: Layer Data (Contd)
LAYER_DATA ipLayer
{
FIELD sip:32; // source IP address
FIELD dip:32; // destination IP address
FIELD vrfId:16; // Virtual Route Forwarding Id derived from table lookups.
FIELD isTCP:1; // Is this a TCP packet
FIELD isUDP:1; // Is this a UDP packet
...
...
}
May contain data derived during pipe line processing.
Anything that we care about that layer.

## Slide 13: Packet Template Definition Examples
PACKET_TEMPLATE IPv4overEthTemplate
{
LAYER_DATA ethLayer; // Extracted data from the ethernet header
LAYER_DATA ipLayer; // Extracted data from the IP header
}
PACKET_TEMPLATE IPv4overDot1qTemplate
{
LAYER_DATA dot1qEthLayer; // Extracted data from the 802.1q header
LAYER_DATA ipLayer; // Exctracted data from the IP header
}
Each definition represents a supported packet classification.

## Slide 14: Parser Definition: EthParser
PARSER ethParser((inputPort == 1)||(inputPort == 8)|| ...) // Ports 1 and 8 are ethernet ports
{
ethLayer.dMac = ethHeader.dMac;
ethLayer.sMac = ethHeader.sMac;
if (ethHeader.eType == 0x8100)
{ // Detected .1q tag
dot1qExtract.dot1qTag = dot1qHeader.dot1qTag;
if (dot1qHeader.eType == 0x0800)
{ // Detected IPv4overDot1qTemplate, one of the accepted packet templates
packetTemplate = IPv4overDot1qTemplate;
IPv4overDot1qTemplate.ipLayer.sip = ipv4OverDot1qHeader.sourceIp;
IPv4overDot1qTemplate.ipLayer.dip = ipv4OverDot1qHeader.destIp;
if (ipv4OverDot1qHeader.protocol == IP_PROTOCOL_UDP)
{ // Upper layer is UDP
IPv4overDot1qTemplate.ipLayer.isUDP = true;
} else if (ipv4OverDot1qHeader.protocol == IP_PROTOCOL_TCP)
{ // Upper layer is TCP
IPv4overDot1qTemplate.ipLayer.isTCP = true;
}
NEXT(RouterEngineKeyFormatter, ...);
break; // Parsing complete
} else {/*Handle formats other than IPv4*/}
} else {/*Handle other ether types*/}
} // end of definition

## Slide 15: Table Definition Example: IPv4UcRouteTable
TABLE IPv4UcRouteTable (depth=1000)
{
FIELD pktCmd :2;
FIELD egressInterface:16;
...
...
};
KEY IPv4UcRouteTable
{
FIELD ipAddress :32;
FIELD vrfId :16;
};
LOOKUP IPv4UcRouteTable(0)
{
// LPM search code for IPv4UcRouteTable
NEXT(RouterEnginePostLookup);
} // End of definition

## Slide 16: Key Formatter Definition: Route Engine Key Formatter
KEY_FORMATTER RouterEngineKeyFormatter(false)
{
if (packetTemplate == IPoverDot1qTemplate)
{
IPv4UcRouteTable.ipAddress = IPoverDot1qTemplate.ipLayer.dip;
IPv4UcRouteTable.vrfId = IPoverDot1qTemplate.ipLayer.vrfId;
NEXT = IPv4UcRouteTable;
break;
}
else if (packetTemplate == MPLSoverEthTemplate)
{
MPLSLabelTable.Label = MPLSoverEthTemplate.Label;
NEXT = MPLSLabelTable;
break;
}
else {/*Build Table Keys for other tables in the router engine*/}
} // End of definition

## Slide 17: Post Lookup Processing Definition: Route Engine Post Lookup
POST_LOOKUP RouterEnginePostLookup(WAIT(IPv4UcRouteTable, MPLSLabelTable ...))
{
if (IPv4UcRouteTable.hit == true)
{
pktCmd = IPv4UcRouteTable.pktCmd;
egressInterface = IPv4UcRouteTable.egressInterface;
NEXT(moreProcessing);
break;
}
else if (MPLSLabelTable.hit == true)
{
pktCmd = MPLSLabelTable.pktCmd;
egressInterface = MPLSLabelTable.egressInterface;
NEXT(moreProcessing);
break;
}
else {/*Process the results from other tables*/}
} // end of definition

## Slide 18: Packet Update Definition: Router Update IP over Ethernet
PACKET_UPDATE RouterUpdateIPv4OverEth(0)
{
ipv4OverEthHeader.ttl = ipv4OverDot1qHeader.ttl – 1;
ipv4OverEthHeader.ethHeader.sMac = ethLayer.sMac;
ipv4OverEthHeader.ethHeader.dMac = ethLayer.dMac;
ENQUEUE(egressQueueId);
} // end of definition

## Slide 19: PIFL Intermediate Representation: What it is
Its ‘Intermediate’, not high level.
It’s a ‘Representation’, not a language.
Acts as a ‘target’ for high level languages to write code for.
Independent of high level languages and their syntaxes.
Provides a structured ‘source’ representation for hardware compilers.
Independent of hardware technologies (CPU, FPGA, ASIC etc).
Virtualizes the device and provides addressability into its resources.

## Slide 20: PIFL Intermediate Representation: Basic Requirements
Must allow representation of high level language code without loss of information:
  Must allow representation for data units (variables and structures).
  Must allow representation for statements.
  Must allow representation for ALU operations.
  Must allow representation for conditional execution.
  Must allow representation for parallel execution.
  Must allow representation for sequential dependencies.
Must allow representation for switch primitives.

## Slide 21: PIFL Intermediate Representation: AdvancedRequirements
Must allow incremental updates for run time redefinition of the hardware.
  Add a new table without affecting existing traffic.
  Add a new packet template for parser without affecting existing traffic.
  Define a new Engine to test experimental protocols in production environment.
  Hitless upgrade of an Engine by creating new one first and switching to it.
  Create a virtual ‘slice’ of the chip using spare resources.

## Slide 22: PIFL Intermediate Representation: Sample primitives
Must allow representation for switch primitives.
  Parser (PIFL provides keyword PARSER to define this primitive)
  Table key formatters (PIFL Ex: KEY_FORMATTER)
  Table lookups (PIFL Ex: LOOKUP)
  Post lookup processing (PIFL Ex: POST_LOOKUP)
  Modify packet headers (PIFL Ex: PACKET_UPDATE)
  Queue the packet to egress (PIFL Ex: ENQUEUE)
  Hash Engines (PIFL Ex: HASH)
  Checksum Engines (PIFL Ex: CHKSUM)
  The address space where packets reside (PIFL Ex: PACKET_HEADER)
  The address space for preliminary packet context (PIFL Ex: STATIC_CTX)
  The address space for user defined packet context (PIFL Ex: DYNAMIC_CTX)
  The address space for layer specific data (PIFL Ex: LAYER_DATA)
  The address space for table definitions (PIFL Ex: TABLE)
  The address space for table lookup keys (PIFL Ex: KEY)

## Slide 23: PIFL Intermediate Representation: Benefits
Defined as a Database Schema.
Lets us define primitives in a consistent, table based format.
Allows us to use transaction based updates.
Allows incremental updates.
Might fit in well with Open Flow TTPs.

## Slide 24: PIFL IR Representation for Address Spaces: Symbol Tables.
Symbol Table:
ID | Symbol | Primitive Type | StartBit | BitLength
1 | ipv4OverDot1qHeader.dot1qHeader | Packet Header | 0 | 144
2 | IPOverEthTemplate.ipLayer | Layer Data | 112 | 160
3 | ipv4OverEthHeader.dip | Packet Header | 128 | 32
4 | ingressPort | ingressPort | 0 | 8
5 | IPv4UcRouteTable.egressInterface | Tables | 512 | 16

## Slide 25: PIFL IR Representation for Operations: Prefix Stacks
For Copy of fields
  We use prefix (Polish) notation. This is standard and unambiguous:
    Ip.protocol = 89 
ALU Operations
  Same as above. We use prefix notation.
    Ip.ttl = ip.ttl – 1 
= | Ip.protocol | 89
= | Ip.ttl | - | Ip.ttl | 1

## Slide 26: PIFL IR Representation of Prefix Stacks
ID | Symbol | Primitive Type | Value | NextElem
1 | = | Operator | 1 | 2
2 | ipv4Header.protocol | Packet Header | 112 | 3
3 | 89 | Constant | 89 | NULL
ID | Symbol | Primitive Type | Value | NextElem
4 | = | Operator | 1 | 5
5 | ipv4Header.ttl | Packet Header | 115 | 6
6 | - | Operator | 2 | 7
7 | ipv4Header.ttl | Packet Header | 115 | 8
8 | 1 | Constant | 1 | NULL
ipv4Header.ttl = ipv4Header.ttl - 1
ipv4Header.protocol = 89

## Slide 27: Grouping of Statements into Code Blocks
ID | Symbol | Primitive Type | Value | NextElem
1 | = | Operator | 1 | 2
2 | ipv4Header.protocol | Packet Header | 112 | 3
3 | 89 | Constant | 89 | NULL
4 | = | Operator | 1 | 5
5 | ipv4Header.ttl | Packet Header | 115 | 6
6 | - | Operator | 2 | 7
7 | ipv4Header.ttl | Packet Header | 115 | 8
8 | 1 | Constant | 1 | NULL
10 | statement0 | Statement | 1 | 11
11 | statement1 | Statement | 4 | NULL
Statements can be linked together into Code Blocks using recursive definitions using Type value of ‘Code’.
The ID 10 below represents {ipv4Header.protocol = 89; ipv4Header.ttl = ipv4Header.ttl - 1}
Code Blocks can be further nested into bigger code blocks the same way.

## Slide 28: Representation for prefix stack for Conditions
The ID 1 in the table below represents the following logical expression:
(((packet.isIPv4 == true) && (ipv4Header.protocol == 2)) || ((packet.isIPv6 == true) && (ipv6Header.protocol == 1)))
The Prefix notation of the above expression is give below:
||, &&, ==, packet.isIPv4, true, ==, ipv4Header.protocol, 2, &&, ==, packet.isIPv6, true, ==, ipv6Header.protocol, 1
ID | Symbol | Primitive Type | Value | NextElem
1 | ¦¦ | Operator | 11 | 2
2 | && | Operator | 12 | 3
3 | == | Operator | 10 | 4
4 | packet.isIPv4 | Layer Data | 201 | 5
5 | true | Constant | 1 | 6
6 | == | Operator | 10 | 7
7 | ipv4Header.protocol | Layer Data | 112 | 8
8 | 2 | Constant | 2 | 9
9 | && | Operator | 12 | 10
10 | == | Operator | 10 | 11
11 | packet.isIPv6 | Layer Data | 202 | 12
12 | true | Constant | 1 | 13
13 | == | Operator | 10 | 14
14 | ipv6Header.protocol | Layer Data | 212 | 15
15 | 1 | Constant | 1 | NULL

## Slide 29: Nesting of Conditions
ID | Symbol | Primitive Type | Value | NextElem
1 | == | Operator | 10 | 2
2 | packet.isIPv4 | Layer Data | 201 | 3
3 | true | Constant | 1 | NULL
4 | == | Operator | 10 | 5
5 | ipv4Header.protocol | Layer Data | 112 | 6
6 | 2 | Constant | 2 | NULL
7 | Condition1 | Condition | 1 | 8
8 | Condition2 | Condition | 4 | NULL
Nested Conditions can be expressed by recursive definitions using Type value of ‘Condition’. The individual ‘Condition’s connected together using ‘&&’.
This means that all of the ‘Condition’s in the list must evaluate to ‘true’ in order to make the nested condition ‘true’.
The condition id 7 above recursively evaluates to: ((packet.isIPv4 == true) && (ipv4Header.protocol == 2))

## Slide 30: PIFL IR Representation for Control Flow: Threads
Threads can be represented as code blocks and conditions to execute them:
Code
Block0
Code
Block1
Condition0
Condition1
Condition2
Statement0
Statement1
Condition0
Condition1
Statement2
Statement0
Statement1
The code blocks will represent sequentially executed code blocks in the source code.
Each code block has a list of statements that constitute the code block.
Code blocks can be nested.
For if() blocks, the block can be tagged with a list of conditions that needs to be satisfied for the block to be executed.
The conditions list for the first block can denote the preconditions for executing the thread, if any.

## Slide 31: PIFL IR Representation for a Thread
ID | Symbol | Primitive Type | StatementIdx | ConditionIdx | NextElem
1 | codeBlock0 | Statement | 100 | 0 | 2
2 | codeBlock1 | Statement | 200 | 202 | 3
3 | codeBlock2 | Statement | 300 | 128 | 4
4 | KeyBuild | Key Formatter | 400 | 0 | NULL
The following represents a Thread of primitive type Key Formatter.

## Slide 32
Thank You!